## Slide 1
Chapter 2:
Network Protocol Models

## Slide 2
Outline
Protocol and Standard
Layered tasks
Internet protocol suites
ISO's OSI model

## Slide 3
The Need of Protocols
The scenario: Two people living in two different places want to speak together, what do they need:
  Links
  Phones
  Speak the same langauge
Two computers want to communicate together?

## Slide 4
Protocols and Standards
Protocol
  A set of rules governing data communications
    Syntax: format of data block
    Operation: Interaction between senders and recievers
Standards
  De facto (in practice) standards
 not approved but widely adopted
  De jure (in law) standards
 approved by an organization

## Slide 5
Standards Organizations
Creation Committees
  ISO, ITU-T, ANSI, IEEE, EIA
Forums
Regulatory Agencies

## Slide 6
Layered Tasks
Computer networks are complex systems
  Tasks involve varieties of hardware and software components, and protocols
Networking task is divided into several subtasks, or layers

## Slide 7
Real World Example
Communication between managers of two companies
Communicate

## Slide 8
What Actually Happens
Communication takes place thru many layers
Logical communication
Secretary:
types a letter
Delivery boy:
drops the letter
Secretary:
reads and reports
the message
Delivery boy:
takes the letter
Post office:
Processes and routes the letter
Postal truck

## Slide 9
Layer Model
Layer N uses services provided by Layer N-1
Layer N
Layer N
Using
services
Providing
services
Logical
communication path
HOST A
HOST B
Layer N-2
Layer N-2
Layer N-1
Layer N-1
Virtual Communication System
Layer N protocol

## Slide 10
Why Layers?
Guidelines for protocol developments
  Reference model
Modularity
  Eases maintenance and updating of systems
  A change in one layer is transparent to the rest
Is layering always the best thing to do?
  Maybe not  cross-layer optimization

## Slide 11
Internet Layer Model
The Internet Protocol Stack
Application Layer
Transport Layer
Network Layer
Data Link Layer
Physical Layer
User
Transmission
Medium
Hardware
Software

## Slide 12
Application Layer
The only layer to interact with user
Responsible for providing services to the user
SMTP
HTTP
FTP
SMTP
HTTP
FTP
Data
Data
H5
Application
Layer
to Transport
from Transport
Data
H5
Data
Logical communication

## Slide 13
Transport Layer
Duties/services
  Port addressing
  Segmentation and reassembly
  Connection control
  Flow control (end-to-end)
  Error control (end-to-end)
Responsible for delivery of a message
from one process to another

## Slide 14
Transport Layer
Transport
Layer
Data
Data1
Data2
Data3
H4
H4
H4
to Network
Data
Data1
Data2
Data3
H4
H4
H4
from Network
(segments)
Process
Process
…
Process
Process
…
PORT #
PORT #

## Slide 15
Network Layer
Duties/services
  Logical addressing
  Routing
Responsible for the delivery of packets
from the original source to the destination

## Slide 16
Network Layer
Network
Layer
Data
from Transport
to Data Link
Data
to Transport
from Data Link
Data
H3
Data
H3
(packet)

## Slide 17
Network Layer
Network 1
Network 6
Network 5
1.1
1.2
6.6
6.1
6.3
5.7
5.2
Network 3
3.8
3.3
Router
Data
1.1
5.7
1.1, 1.2, 6.1, 5.7, ... are logical addresses
R1
R3
R2

## Slide 18
Data Link Layer
Duties/services
  Framing
  Physical addressing
  Flow control (hop-to-hop)
  Error control (hop-to-hop)
  Access control
Responsible for transmitting frames
from one node to the next

## Slide 19
Data Link Layer
Data Link
Layer
Data
from Network
to Physical
Data
to Network
from Physical
Data
H2
Data
H2
(frame)
T2
T2

## Slide 20
Data Link Layer
3B
A3, 3B, 82, 9F, ... are physical addresses
9F
82
A3
Data
9F
T2
A3
Data
H2

## Slide 21
Data Link Layer
Network 1
Network 6
Network 5
1.1
1.2
6.6
6.1
6.3
5.7
5.2
Network 3
3.8
3.3
Data
1.1
5.7
97
32
25
79
62
54
74
12
88
Data
1.1
5.7
25
97
Data
1.1
5.7
62
79
Data
1.1
5.7
74
54
R1
R3
R2

## Slide 22
Physical Layer
Duties/services
  Physical characteristics of interfaces and media
  Representation of bits
  Data rate (transmission rate)
  Synchronization of bits
Responsible for transmitting individual bits
from one node to the next

## Slide 23
Physical Layer
Physical
Layer
Data
from Data Link
to Data Link
Data
01001011
01001011
Transmission medium
(bits)

## Slide 24
The Big Picture
L5 data
H5
L4 data
H4
L3 data
H3
L2 data
T2
H2
0111011010101001010101001
L5 data
H5
L4 data
H4
L3 data
H3
L2 data
T2
H2
0111010101010010101010101
5
4
3
2
1
5
4
3
2
1
Transmission medium

## Slide 25
Network
D.L.
P.L.
D.L.
P.L.
Network
D.L.
P.L.
D.L.
P.L.
Internet Model
Application
Transport
Network
Data Link
Physical
Application
Transport
Network
Data Link
Physical
Transmission medium
sender
router
router
receiver

## Slide 26
Internet Model

## Slide 27
Protocol Suites
A set of protocols must be constructed
  to ensure that the resulting communication system is complete and efficient
Each protocol should handle a part of communication not handled by other protocols
How can we guarantee that protocols work well together?
  Instead of creating each protocol in isolation, protocols are designed in complete, cooperative sets called suites or families

## Slide 28
Internet Protocol Suite
Layer | Protocols
Application | HTTP, FTP, Telnet, SMTP, ...
Transport | TCP, UDP, SCTP, ...
Network | IP (IPv4), IPv6, ICMP, IGMP, ...
Data Link | Ethernet, Wi-Fi, PPP, ...
Physical | RS-232, DSL, 10Base-T, ...

## Slide 29
OSI Model
OSI – Open Systems Interconnection
Developed by the International Standards Organizations (ISO)
Two additional layers
  Presentation layer
  Session layer
7.Application Layer
6.Presentation Layer
5.Session Layer
4.Transport Layer
3.Network Layer
2.Data Link Layer
1.Physical Layer
User
Transmission
Medium

## Slide 30
Session Layer
Duties/services
  Interaction management
 Simplex, half-duplex, full-duplex
  Session recovery
Responsible for establishing, managing and terminating connections between applications

## Slide 31
Presentation Layer
Duties/services
  Data translation
  Encryption
  Decryption
  Compression
Responsible for handling differences in
data representation to applications

## Slide 32
OSI Layers in Real World
transmission medium
Reads the
message
Summarizes or
translates letter
Opens letter
Withdraws letter
from mailbox
Checks address
and sorts letter
Unpacks
packages
Unloads
from truck
Handwrites
a message
7.Manager
Prepares
final version
6.Assistant
Provides address
and packs letter
5.Secretary
Delivers letter
to post office
4.Driver
Checks address
and sorts letter
3.Postal staff
Packs letters
for certain directions
2.Postal staff
Loads on truck
1.Postal staff
Pictures from Wikipedia